CS349 ASSIGNMENT 2	Rashi Singh
Network Protocol Analysis Using Wireshark	170101052

Q1 : PROTOCOLS USED IN DIFF LAYERS
   Network Layer :

Figure 1: Protocol Hierarchy used by DropBox

       IPv4 : Internet Protocol Version 4 :
IPv4 is a network-layer protocol used in packet-switched	layer networks, such as Ethernet. It provides a logical	connection between network devices by providing	identification for each device and routing data among	them over the underlying network. IP uses best effort	delivery, i.e. it does not guarantee that packets would	be delivered to the destined host, but it will do its best to	reach the destination. Internet Protocol version 4 uses

32-bit logical ddress.
# IPv4 - Packet Structure :

Figure 3: WireShark IPv4 layer packet details

Figure 2: IPv4 Header Structure

VERSION	- (4 bit) Version of the Internet Protocol used
HEADER LENGTH	- (4 bit) Length of the IP header in 32 bit increments.
 **Min length of IP header is 20 bytes, so with 32 bit increments, min value of IHL is 5.
 **Max value of IHL is 15 so with 32 bit increments, max length of IP header is 60 bytes
TYPE OF SERVICE	- Provides an indication of the abstract parameters of the quality of service desired.
TOTAL LENGTH	- (16 bit) Length of the datagram (in bytes), including internet header and data.
IDENTIFICATION	- An identifying value assigned by the sender to help assemble the fragments of a datagram
FLAGS	- (3 bit) Various Control Flags
FRAGMENT OFFSET	- (13 bit) Indicating where in the datagram this fragment belongs.
TIME TO LIVE	- (8 bit) The max time the datagram is allowed to remain in the internet system.
PROTOCOL	- Next level protocol used in the data portion of the internet datagram.
HEADER CHECKSUM	- A checksum on the header only.
SOURCE/DEST ADDRESS	- (32 bit) Addr of the source/destination respectively
Transport Layer :
    TCP : Transport Control Protocol :
TCP is a connection oriented protocol which offers end-to-end packet delivery. TCP ensures reliability by	sequencing bytes with a forwarding acknowledgement number that indicates to the destination, the next byte
 the source expect to receive.It retransmits the bytes not acknowledged with in specified time period.
Dropbox mainly used TCP to send application data mainly due its reliability feature
    TCP - Packet Structure :

Figure 5: WireShark TCP packet details

Figure 4: TCP header structure

SOURCE/DEST PORT	: (16 bit) Fields to identify the end points of the connection.
SEQUENCE #	: (32 bit) Number assigned to the first byte of data in the current message
ACKNOWLEDGEMENT #	: (32 bit) Value of the next sequence # that the sender of the segment is expecting to receive
DATA OFFSET	: Specifies how many 32-bit words are contained in the TCP header.
RESERVED	: (6 bit) Must be zero. This is for future use.
FLAGS	: (6 bit) URG, ACK, PSH, RST, SYN, FIN
WINDOW	: (16 bit) Specifies the size of the sender's receive window
CHECKSUM	: (16 bit) Indicates whether the header was damaged in transit.
URGENT	: pointer (16 bit) Points to the first urgent data byte in the packet.
OPTIONS	: (variable length) Specifies various TCP options.
DATA	: (variable length) Contains upper-layer information.
UDP : User Datagram Protocol :

Figure 6: WireShark UDP packet details
  -	UDP is connectionless and unreliable protocol. It doesn’t require	making a connection with the host to exchange data. Since UDP	is unreliable protocol, there is no mechanism for ensuring that	data sent is received.
  -	UDP is used by the application that typically transmit small	amount of data at one time. UDP datagram consists of the	following : Src/Dest Port, Length, Checksum (like TCP header)

DB-LSP-DISC : DropBox LAN Sync Discovery Protocol :
  -	Dropbox LAN Sync (DB-LSP, a diff protocol) is a feature that allows you to	download files from other computers on your network, saving time and	bandwidth compared to downloading them from Dropbox servers.	Without LAN Sync, these requests would be queued up and sent to the	block server, which would return block data.

Figure 7: WireShark DB-LSP-DISC packet details
  -	For LAN sync to work, the discovery engine is responsible for finding	machines on the network that we can sync with (i.e., machines which	have access to namespaces in common with ours). To do this, each	machine periodically sends and listens for UDP broadcast packets over
port 17500.
The packet contains VERSION of protocol used by PC, TCP PORT of the server (17500), HOST_INT : a random identifier for
the UDP packet to be identified by the receiver, the NAMESPACES** supported.
        **Namespaces are the primitive behind Dropbox’s permissions model. They can be thought of as a directory with
specific permissions. Every account has a namespace which represents its personal Dropbox account

Figure 8: TLS packet exchange flow
 B/w Application, Transport Layer :
  TLSv1.2 : Transport Layer Security
    It is a cryptographic protocol, developed
     from the generalized version of SSL(Secure
     Socket Layer)(now deprecated). It
     provides 3 essential services to the
     applications running above it:

**TLS requires a reliable transport. Hence, it uses TCP	Verification of validity of identity : AUTHENTICATION a)
   Detection of msg tampering, forgery : DATA INTEGRITY b)
  A mechanism to obfuscate what is sent from one host to another : ENCRYPTION c)
PACKETS for TLSv1.2

Figure 9: Common parameters in TLS packets
The common parameters present in diff. kinds of TLS packets are :

a) VERSION : 16 byte version
b) LENGTH : 16 byte record length,
        formatted in network order
c) CONTENT TYPE : This signifies the types of TLS packets that are recognized. Some of the common types are :
1) HANDSHAKE – Please refer Q4 HANDSHAKE for more detailed info.
2) APPLICATION_DATA – This type of TLS packet has

an additional field k/a Encrypted	Application Data, which is the actual	encrypted data to be sent.

3) CHANGE_CIPHER_SPEC – Used to change the	encryption being used by the client and	server. The message tells the peer that	the sender wants to change to a new set	of keys, which are then created from information exchanged by the handshake protocol.

Q2 : OBSERVED PACKET VALUES :
 IPv4 : Internet Protocol Version 4 :

TCP : Transport Control Protocol :

UDP : User Datagram Protocol :

DB-LSP-DISC : DropBox LAN Sync Discovery Protocol :

TLSv1.2 : Transport Layer Security

Q3 : PROTOCOLS FOR IMP DROPBOX FUNCTIONS :
Q4 : DROPBOX FUNCTIONALITIES, MSGS, HANDSHAKES:

HANDSHAKE - The process that kicks off a communication session that uses TLS encryption. As shown in	Figure 8: TLS packet exchange flow, the handshake takes place in the following seq :
     a)	the two communicating sides exchange	messages to acknowledge each other
     b)	verify each other
     c)	establish the encryption algorithms they will use
     d)	agree on session keys
     In WireShark, Client and Server Hello

Q5 : TRACE STATISTICS AT DIFF TIMES :

//TODO: GRAPH LAGA DIYO MANN KRE TO
//TODO: METHOD TO CALCULATE BHI LIKH DIYO
Q6 : RESOLVED HOSTS :